## Slide 1: Common Wine Faults and Their Impacts
Dr Eric Wilkes
Australian Wine Research Institute

## Slide 2: Wine is a manufactured natural product
So by definition, things will go wrong.
One of the roles of the AWRI is to investigate such manufacturing issues.

## Slide 3
The AWRI

## Slide 4: World class people
The gap…

## Slide 5: World class facilities
Notes: Sample numbers continue to rise, and rise and rise

## Slide 6: Industry owned business model
Labs
Extension
Research
Development
Services to Industry
Industry
Notes: CS is a significant part of the AWRI (21 staff) and one of it greatest strengths is being an integrated part of the organisation.

## Slide 7: So what do we get asked?
~5,000 requests for technical assistance per annum; ~20 every day
>1,000 problem samples investigated per annum
Chart: Keyword
| Sustainability | Smoke | Agrochemical | Taint & Contaminations | Requirements | Haze/Deposit | Brett | Organoleptic | Analysis Methods | Other | Winemaking Practices | Vineyard Practices | Extension | Microbiological | Viticulture - general | Cold Stability | Pest Fungal/Viral | Stuck Fermentation | Acids | Analysis Interpretation | Bottling Advice | SO2 | Storage & Transport | Filtration | Healthy effects
GreatNSW/ACT | 13 | 5 | 12 | 9 | 8 | 6 | 6 | 5 | 5 | 3 | 4 | 5 | 2 | 9 | 8 | 8 | 4 | 3 | 5 | 5 | 9 | 1 | 4 | 6
SA Central | 83 | 23 | 30 | 15 | 27 | 15 | 13 | 16 | 14 | 23 | 14 | 14 | 19 | 10 | 21 | 4 | 12 | 5 | 4 | 7 | 4 | 7 | 4 | 5
GreatVIC | 18 | 21 | 21 | 16 | 6 | 13 | 14 | 9 | 1 | 11 | 18 | 8 | 6 | 8 | 2 | 9 | 17 | 7 | 3 | 7 | 6 | 1
WA | 26 | 24 | 19 | 11 | 9 | 4 | 4 | 8 | 4 | 1 | 7 | 3 | 1 | 2 | 4 | 4 | 3 | 3 | 3 | 4 | 1 | 1 | 1
TAS | 5 | 19 | 2 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 1 | 1 | 5 | 2 | 1 | 1 | 1 | 3 | 1
QLD | 1 | 1 | 2 | 2 | 4 | 1 | 1 | 2 | 1 | 3 | 2 | 1 | 1
SA North | 30 | 28 | 5 | 23 | 6 | 17 | 11 | 6 | 8 | 6 | 4 | 3 | 9 | 2 | 3 | 3 | 6 | 4 | 4 | 3 | 3 | 1
Other | 3 | 2 | 2 | 2 | 4 | 2 | 3 | 3 | 4 | 8 | 4 | 1 | 1 | 2 | 2 | 1 | 1 | 4 | 2 | 5 | 3
Sumcheck
Limestone Coast | 18 | 3 | 5 | 2 | 4 | 1 | 1 | 2 | 1 | 2 | 3 | 3 | 3 | 2 | 1
Murray Valley | 9 | 6 | 1 | 9 | 2 | 5 | 2 | 1
Riverina | 1 | 1 | 10 | 5 | 8 | 1 | 1 | 4 | 5 | 1 | 2 | 1 | 2 | 1 | 9 | 2 | 2 | 4 | 3 | 2 | 1 | 5

## Slide 8: So what are the major fault investigations?

## Slide 9: Wine Hazes
~10% all winemaking investigations
are protein/copper-protein related

## Slide 10: Hazes
Protein
Pinking
Yeast
Polysaccharides
Iron
Oxidised phenolics
Copper/Protein

## Slide 11: Wine Hazes are caused by naturally occurring proteins

## Slide 12: Crystalline deposits

## Slide 13: Crystalline type deposits
Potassium L bitartrate (KHT)
Calcium L and DL tartrate
Quercetin
Diatomaceous earth
Cork wax

## Slide 14: Taints

## Slide 15: Oxidation and Reduction
O2
Oxidation
Reduction
browning
bruised apple
cooked
tired
rotten eggs
cabbage
burnt rubber
sewage
complexity
blackcurrant
struck flint
complexity
softening
integration
Notes: Lets call them what they really are, unpleasant stinks!
Research has shown that they are linked to a range of factors.
The amount of copper and iron in the wine
The yeast used and the nature of the ferment
The amount of oxygen seen at various times of the wines life.
Importantly, some research has shown that for a some wine, lower levels of oxygen in bottle (for instance as seen with a saran/tin screwcap) can lead to higher amounts of the compounds responsible for the stinky odours.

## Slide 16: Smoke Taint
Changes in climate are leading to increased fire events.
smoky, phenolic, medicinal
The compounds responsible are generally the same introduced by barrel aging
Notes: Guaiacol
(threshold: 20 ng/L, described as smoky, phenolic, medicinal)—a component of smoke (eg. Leigh Francis’ samples earlier today). Associated with high toast level in barrels; formed during barrel toasting process, can then be extracted into wine at a typical concentration of 30–40 g/L. Also possible component of cork taint – the primary off-flavour compound in faulty corkwood affected by a yellow discolouration. It is formed by soil bacteria such as Streptomyces sp. (which grow on lignin in the corkwood) and other microflora including some moulds (Amon et al).
Guaiacol is present in corkwood, but the quantities formed by the degradation of lignin under normal processing conditions for wine corks would be insufficient to cause a taint in cork. Therefore, guaiacol is not a significant cause of cork taint in Australia.
Guaiacol is often below its flavour threshold concentration and influences wine aroma by acting in combination with other components. (Synergism – response to several components is greater than the sum of the individual contributions.

## Slide 17: Cork Taint
Notes: They never stop

## Slide 18: Microbiological issues
Wine does not pose a risk as far as pathogens is concerned.
However, some yeast and bacteria can cause issue before, during and immediately after fermentation.
Oenococcus oeni, Pediococcus, Lactobacillus, Brettanomyces
All have the potential to damage the quality of wine
But none produce dangerous metabolites in wine.
The taint compounds are usually present in incredibly low concentrations.

## Slide 19: So what are wine faults
In the vast majority of cases they are naturally occurring wine components.
They become an issue when they become out of balance with the normal expectation due to processing or climatic effects.
The major impact is on consumer acceptance .
They do not pose any risk to human health and safety.