## Slide 1: Ring Test Program 2017 Results
Dr Eric Wilkes
Australian Wine Research Institute

## Slide 2: Background
In 2015 the APEC Wine Regulatory forum commissioned a ring test program to evaluate the degree of variability between laboratories in APEC economies who were involved in the testing of common wine components.
The results were far from ideal.

## Slide 3: 2016 Ring Test Results
 | White |  | Red | 
 | APEC | IWAG | APEC | IWAG
Mean | 115.66 | 125 | 67.03 | 63
Standard Deviation | 21.99 | 6 | 11.87 | 5
Total Sulfur Dioxide

## Slide 4: Background
In 2015 the APEC Wine Regulatory forum commissioned a ring test program to evaluate the degree of variability between laboratories in APEC economies who were involved in the testing of common wine components.
The results were far from ideal.
Based on the these results it was decided to continue the ring test program and run a series of workshops on the best practice in wine laboratory testing.

## Slide 5: Laboratory Method Workshops
A workshop/tutorial covering the best practice for methodology for 4 common wine analytes was held prior to the International Wine Technical Summit( IWTs) in San Luis Obispo 2016 and was attended by 55 wine regulators, laboratory scientists and wine industry representatives from six WWTG economies and 11 APEC economies.
In 2017 in at the Hanoi APEC WRF a work shop on “The core elements of a strong laboratory management system” was presented highlighting the base requirements for laboratory analysis.
In 2018 at the Lodi IWTS meeting a further workshop was held for attendees looking at “Fit for Purpose Analysis” and highlighted the importance of robust method validation.

## Slide 6: The ring test program
The program is an opportunity for laboratories from different economies to compare the results for typical wine analysis between different laboratories.
As part of a larger wine proficiency testing program it also allows economies to compare their laboratories results to those typically achieved for the wine tested.
In 2018, 22 nominated laboratories from 14 different economies.
There are still significant difficulties being encountered shipping wine samples to a number of economies which will need resolution going forward.

## Slide 7: 2018 Program
For 2018 the APEC ring test program was fully integrated into the Interwinery Analysis Group Proficiency program.
This is a large wine specific program with over 200 participating laboratories.
It consists of 6 separate rounds of testing, 2 red wines, 2 white wine and 2 rose wine rounds.
Laboratories can submit analytical results for any of the common wine analysis that is done.
All data is entered online and collated anonymously.
Within 2 weeks of the closure of each testing window an online report is available.
Currently only the first 5 rounds of testing have been completed.

## Slide 8: Participants 2018
Economy | Labs | Samples delivered | Results Submitted
Australia | x2 | yes | yes
New Zealand | x2 | yes | yes
Canada | x2 | yes | yes
Philippines | x1 | yes | 
Indonesia | x2 | yes | yes
Vietnam | x2 | yes | yes
PNG | x2 | yes | yes
Chile | x1 | no | -
USA | x2 | yes | yes
Japan | x2 | yes | yes
China | x2 | yes | no
Peru | x1 | no | -
Mexico | x1 | yes | yes
Thailand | x1 | yes | yes

## Slide 9: Alcohol
wine | Analyte | APEC mean | APEC stdev | APEC count | APEC CV | IWAG mean | IWAG stdev | IWAG count | IWAG CV
red | Alcohol | 13.25 | 0.67 | 20 | 5.07% | 13.72 | 0.52 | 362 | 3.82%
white | Alcohol | 12.18 | 0.33 | 24 | 2.67% | 12.34 | 0.19 | 342 | 1.57%
rose | Alcohol | 11.58 | 0.25 | 26 | 2.18% | 11.70 | 0.19 | 344 | 1.62%
 |  |  |  | Average | 3.31% |  |  |  | 2.34%
Chart: Comparative Performance, Alcohol
| red | white | rose
APEC CV | 0.050665 | 0.026724 | 0.021809
IWAG CV | 0.038245 | 0.015739 | 0.016151

## Slide 10: Alcohol

## Slide 11: Total Sulfur Dioxide
wine | Analyte | APEC mean | APEC stdev | APEC count | APEC CV | IWAG mean | IWAG stdev | IWAG count | IWAG CV
red | TSO2 | 64.1 | 15.9 | 14 | 24.77% | 56.2 | 7.2 | 370 | 12.89%
white | TSO3 | 92.1 | 12.8 | 16 | 13.94% | 87.9 | 6.4 | 350 | 7.23%
rose | TSO4 | 116.4 | 37.0 | 18 | 31.78% | 127.4 | 11.0 | 346 | 8.65%
 |  |  |  | Average | 23.50% |  |  |  | 9.59%
Chart: Comparative performance, Total SO2
| red | white | rose
APEC CV | 0.24769 | 0.13939 | 0.3178
IWAG CV | 0.12891 | 0.072295 | 0.086507

## Slide 12: Total Sulfur Dioxide

## Slide 13: Titratable Acidity
wine | Analyte | APEC mean | APEC stdev | APEC count | APEC CV | IWAG mean | IWAG stdev | IWAG count | IWAG CV
red | TA | 5.47 | 0.13 | 10 | 2.35% | 5.41 | 0.33 | 350 | 6.18%
white | TA | 5.49 | 0.45 | 10 | 8.23% | 5.20 | 0.30 | 324 | 5.81%
rose | TA | 5.95 | 0.28 | 10 | 4.78% | 5.79 | 0.27 | 322 | 4.64%
 |  |  |  | Average | 5.12% |  |  |  | 5.54%
Chart: Comparative performance, Titratable Acidity
| red | white | rose
APEC CV | 0.02354 | 0.082275 | 0.047762
IWAG CV | 0.061763 | 0.058147 | 0.04643

## Slide 14: Titratable Acidity

## Slide 15: Reducing Sugar
wine | Analyte | APEC mean | APEC stdev | APEC count | APEC CV | IWAG mean | IWAG stdev | IWAG count | IWAG CV
red | Reducing sugars | 3.45 | 1.08 | 8 | 31.28% | 2.91 | 0.77 | 110 | 26.37%
white | Reducing sugars | 3.99 | 0.62 | 12 | 15.62% | 4.09 | 0.50 | 116 | 12.27%
rose | Reducing sugars | 20.28 | 0.94 | 14 | 4.64% | 20.15 | 1.42 | 114 | 7.07%
 |  |  |  | Average | 17.18% |  |  |  | 15.23%
Chart: Comparative performance, Reducing Sugar
| red | white | rose
APEC CV | 0.31281 | 0.15624 | 0.04635
IWAG CV | 0.26368 | 0.12271 | 0.070655

## Slide 16: Reducing Sugar

## Slide 17: Glucose + Fructose
wine | Analyte | APEC mean | APEC stdev | APEC count | APEC CV | IWAG mean | IWAG stdev | IWAG count | IWAG CV
red | G+F | 1.44 | 0.24 | 6 | 16.29% | 1.29 | 0.32 | 300 | 25.12%
white | G+F | 3.43 | 0.65 | 6 | 19.08% | 2.90 | 0.46 | 272 | 15.82%
rose | G+F | 20.79 | 2.80 | 8 | 13.46% | 19.00 | 2.93 | 266 | 15.41%
 |  |  |  | Average | 16.28% |  |  |  | 18.78%
Chart: Comparative performance, Glucose + Fructose
| red | white | rose
APEC CV | 0.16294 | 0.19076 | 0.13462
IWAG CV | 0.25121 | 0.1582 | 0.15408

## Slide 18: Glucose + Fructose

## Slide 19: Specific Gravity
wine | Analyte | APEC mean | APEC stdev | APEC count | APEC CV | IWAG mean | IWAG stdev | IWAG count | IWAG CV
red | S.G. | 0.9940 | 0.0022 | 12 | 0.22% | 0.9926 | 0.0038 | 274 | 0.38%
white | S.G. | 0.9923 | 0.0003 | 20 | 0.03% | 0.9920 | 0.0020 | 268 | 0.20%
rose | S.G. | 0.9999 | 0.0003 | 20 | 0.03% | 0.9999 | 0.0021 | 280 | 0.21%
 |  |  |  | Average | 0.09% |  |  |  | 0.27%
Chart: Comparative performance, Specific Gravity
| red | white | rose
APEC CV | 0.0021953 | 0.00028879 | 0.00026606
IWAG CV | 0.0038425 | 0.0020107 | 0.0021149

## Slide 20: Specific Gravity

## Slide 21: Copper
wine | Analyte | APEC mean | APEC stdev | APEC count | APEC CV | IWAG mean | IWAG stdev | IWAG count | IWAG CV
red | Copper | 64.9 | 6.6 | 6 | 10.15% | 62.4 | 22.2 | 52 | 35.58%
white | Copper | 75.2 | 4.3 | 6 | 5.72% | 68.3 | 11.2 | 54 | 16.33%
rose | Copper | 116.1 | 32.6 | 8 | 28.12% | 100.3 | 21.4 | 54 | 21.35%
 |  |  |  | Average | 14.67% |  |  |  | 24.42%
Chart: Comparative performance, Copper
| red | white | rose
APEC CV | 0.10155 | 0.057223 | 0.28122
IWAG CV | 0.35582 | 0.16328 | 0.21352

## Slide 22: Copper

## Slide 23: Iron
wine | Analyte | APEC mean | APEC stdev | APEC count | APEC CV | IWAG mean | IWAG stdev | IWAG count | IWAG CV
red | Iron | 2.50 | 0.55 | 8 | 21.81% | 2.12 | 0.31 | 54 | 14.62%
white | Iron | 1.30 | 0.31 | 10 | 23.71% | 1.03 | 0.20 | 54 | 19.59%
rose | Iron | 1.26 | 0.29 | 10 | 23.16% | 1.42 | 0.20 | 54 | 14.25%
 |  |  |  | Average | 22.89% |  |  |  | 16.15%
Chart: Comparative performance, Iron
| red | white | rose
APEC CV | 0.21809 | 0.23709 | 0.2316
IWAG CV | 0.14616 | 0.19589 | 0.1425

## Slide 24: Iron

## Slide 25: Manganese
wine | Analyte | APEC mean | APEC stdev | APEC count | APEC CV | IWAG mean | IWAG stdev | IWAG count | IWAG CV
red | Manganese | 2.28 | 0.18 | 6 | 8.11% | 2.16 | 0.27 | 38 | 12.34%
white | Manganese | 1.60 | 0.54 | 8 | 34.13% | 1.38 | 0.28 | 38 | 20.06%
rose | Manganese | 1.13 | 0.53 | 8 | 46.51% | 1.33 | 0.27 | 36 | 20.71%
 |  |  |  | Average | 29.59% |  |  |  | 17.70%
Chart: Comparative performance, Manganese
| red | white | rose
APEC CV | 0.081119 | 0.34132 | 0.46515
IWAG CV | 0.1234 | 0.20063 | 0.20709

## Slide 26: Manganese

## Slide 27: Methanol
wine | Analyte | APEC mean | APEC stdev | APEC count | APEC CV | IWAG mean | IWAG stdev | IWAG count | IWAG CV
red | Methanol | 160.3 | 41.5 | 12 | 25.92% | 161.7 | 31.2 | 22 | 19.30%
white | Methanol | 54.8 | 11.6 | 10 | 21.13% | 56.4 | 10.7 | 22 | 18.96%
rose | Methanol | 54.1 | 31.5 | 14 | 58.15% | 51.2 | 24.1 | 24 | 46.98%
 |  |  |  | Average | 35.07% |  |  |  | 28.41%
Chart: Comparative performance, Methanol
| red | white | rose
APEC CV | 0.25922 | 0.21127 | 0.58154
IWAG CV | 0.19303 | 0.18963 | 0.46978

## Slide 28: Methanol

## Slide 29: Are we Improving?
Chart: Reducing Sugar
| 2015 | 2016 | 2017
CV % | 24.7 | 22.5 | 10.1
Chart: Alcohol %
| 2015 | 2016 | 2017
CV % | 1.6 | 5.3 | 1.43
Chart: Total Sulfur Dioxide
| 2015 | 2016 | 2017
CV % | 30.24 | 19.61 | 10.26

## Slide 30: Results to Date
There have been significant improvements in laboratories performance compared to previous rounds.
Still however significant outliers demonstrating the need to continue the program.
It is significant that laboratories which have participated in the wine program long term are performing more consistently than those new to wine ring testing.
The impact of different analytical methods being used is apparent and leads to varied results between laboratories.
Also need to increase the participation rate going forward.
Need to look for alternative sample delivery options
Funding the program in the future must be addressed as APEC WRF funding ends

## Slide 31
Thank You