## Slide 1: Methods Compendium– Alcohol Example Patricia Nedialkova, Ph.D. Chief, Compliance Laboratory U.S. Treasury Department Alcohol and Tobacco Tax and Trade Bureau (TTB) November 13, 2015

## Slide 2: Importance of Sharing Method Information
Method results can stop import shipments resulting in:
  Decline in product quality
  Destruction of product
  Future loss of sales
  Cost and personnel time
Transparency around:
  Regulatory limits
  Methods used to enforce them
  Method performance
can help resolve these issues

## Slide 3: Tbilisi Principle #7: Analytical Levels
When governments implement limits for analytical levels in relation to wine, they should specify the method by which compliance with those limits is confirmed, and should make those limits and methods publicly available.

## Slide 4: Sharing Limits
Economy | Regulations Relevant to Enforcement Using an Alcohol Method | Reference | Internet Link
China | For wines contain ≥7.0% （20℃）alcohol by volume. The degree of alcohol marked on the label and the measured value shall not be more than ±1.0% （%vol） | GB 15037-2006/5.2 | 
 | For low-alcohol wines contain 1.0%--7.0% alcohol by volume. | GB 15037-2006/3.2.7 | 
 | For non-alcohol wines contain 0.5%--1.0% alcohol by volume. | GB 15037-2006/3.2.8 | 
USA | Table wines contain ≥7% and ≤14% alcohol by volume. | 27CFR4.21 (a)2 | http://www.ecfr.gov/cgi-bin/text-idx?
 | The detectable alcohol in table wines must be ±1.5% of the label value. | 27CFR4.36 (b)(1) | http://www.ecfr.gov/cgi-bin/text-idx?
 | Dessert wines contain >14% and ≤24% alcohol by volume. | 27CFR4.21 (a)3 | http://www.ecfr.gov/cgi-bin/text-idx?
 | The detectable alcohol in dessert wines must be ±1.0% of the label value. | 27CFR4.36 (b)(1) | http://www.ecfr.gov/cgi-bin/text-idx?
 | The detectable alcohol in wine based products containing below 7% alcohol must be ±0.75% of the label value. | 27CFR24.257(a)(3) | http://www.ecfr.gov/cgi-bin/text-idx?

## Slide 5: Sharing Methods
Methods submitted with ring test results
Internet link
  http://www.aoacofficialmethod.org/index.php?main_page=product_info&cPath=1&products_id=1882
Reference
  Official Methods of Analysis, 17th Ed., 5th Revision, 1999, AOAC International, Gaithersburg, MD, Method 920.57, "Alcohol in Wines by Volume from Specific Gravity".
Technique
  - Distillation/Density - Fourier Transform Infra-Red (FTIR)
  - Gas Chromatography (GC) - Near Infra-Red (NIR)

## Slide 6: Tbilisi Principle #9: Validation of Analytical Methods
Governments should ensure that, for wine compliance purposes, laboratories use analytical methods that are validated for wine analyses, and that the laboratories are proficient in the use of those methods.

## Slide 7: Sharing Method Performance
Technique | RSD (%)
CODEX fit for purpose method criterion: | ≤ 6
Distillation/Density | 0.2
Fourier Transform Infra-Red (FTIR) | 0.4
Gas Chromatography (GC) | 0.3
Near Infra-Red (NIR) | 0.4

## Slide 8: Statistical Control Chart
Chart: Data Point
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27
Control Limit | 101.6451 | 101.6451 | 101.6451 | 101.6451 | 101.6451 | 101.6451 | 101.6451 | 101.6451 | 101.6451 | 101.6451 | 101.6451 | 101.6451 | 101.6451 | 101.6451 | 101.6451 | 101.6451 | 101.6451 | 101.6451 | 101.6451 | 101.6451 | 101.6451 | 101.6451 | 101.6451 | 101.6451 | 101.6451 | 101.6451 | 101.6451
Warning Limit | 97.4007 | 97.4007 | 97.4007 | 97.4007 | 97.4007 | 97.4007 | 97.4007 | 97.4007 | 97.4007 | 97.4007 | 97.4007 | 97.4007 | 97.4007 | 97.4007 | 97.4007 | 97.4007 | 97.4007 | 97.4007 | 97.4007 | 97.4007 | 97.4007 | 97.4007 | 97.4007 | 97.4007 | 97.4007 | 97.4007 | 97.4007
Mean | 88.912 | 88.912 | 88.912 | 88.912 | 88.912 | 88.912 | 88.912 | 88.912 | 88.912 | 88.912 | 88.912 | 88.912 | 88.912 | 88.912 | 88.912 | 88.912 | 88.912 | 88.912 | 88.912 | 88.912 | 88.912 | 88.912 | 88.912 | 88.912 | 88.912 | 88.912 | 88.912
-2 SD | 80.4233 | 80.4233 | 80.4233 | 80.4233 | 80.4233 | 80.4233 | 80.4233 | 80.4233 | 80.4233 | 80.4233 | 80.4233 | 80.4233 | 80.4233 | 80.4233 | 80.4233 | 80.4233 | 80.4233 | 80.4233 | 80.4233 | 80.4233 | 80.4233 | 80.4233 | 80.4233 | 80.4233 | 80.4233 | 80.4233 | 80.4233
-3 SD | 76.1789 | 76.1789 | 76.1789 | 76.1789 | 76.1789 | 76.1789 | 76.1789 | 76.1789 | 76.1789 | 76.1789 | 76.1789 | 76.1789 | 76.1789 | 76.1789 | 76.1789 | 76.1789 | 76.1789 | 76.1789 | 76.1789 | 76.1789 | 76.1789 | 76.1789 | 76.1789 | 76.1789 | 76.1789 | 76.1789 | 76.1789 | 0 | 0 | 0
Result | 81.6 | 81.6 | 88 | 87 | 89.6 | 83.2 | 92.8 | 91.2 | 89.6 | 88 | 84.8 | 88 | 89.6 | 81.6 | 83.2 | 81.6 | 88 | 88 | 94.4 | 83.2 | 92.8 | 85.4 | 89.6 | 88.5 | 86.4 | 92.16 | 88 | 3.754 | 87.3281 | 0.042987

## Slide 9: Benefits of Control Charts
Gives real time method performance data, as opposed to the snap shot at validation, that can be used to:
  Troubleshoot trends before they become quality failures
  Calculate realistic measurement uncertainties for interpreting results’ compliance
Provides an independent check on standards and calibrations
Meets ISO requirements for demonstrating your method and equipment are under control

## Slide 10: Tbilisi Principle #11: Measurement Uncertainty
Governments should ensure that laboratories provide information on measurement uncertainty regarding their analytical results. Governments should take into account such measurement uncertainty information when interpreting analytical results.

## Slide 11: Sharing Measurement Uncertainty
Technique | MU (%ABV)
Distillation/Density | 0.0
Fourier Transform Infra-Red (FTIR) | 0.1
Gas Chromatography (GC) | 0.1
Near Infra-Red (NIR) | 0.1

## Slide 12: Considering Measurement Uncertainty
Regulation:
%ABV must agree with label within ±1% ABV
Labeled value: 12.0% ABV
Compliant range: 11.0 – 13.0% ABV
Lab measures: 13.1% ABV
Measurement uncertainty: ± 0.1% ABV
True value: 13.0 – 13.2% ABV (95% confidence)
Conclusion: Compliant

## Slide 13: Next Step
Populate the compendium with:
  Regulatory levels
  Validated methods
  Method performance:
    LOD/LOQ for trace methods
    % Recovery for contaminant methods
    Range
    %RSD
    Measurement Uncertainty

## Slide 14: Thank you for your attention!
Feel free to contact me for more information at:
Patricia.Nedialkova@ttb.gov