## Slide 1
Russian Federation: Short review of mandatory tests for imported wine Session 6: Enhanced Risk Controls National Wine Centre November 13, 2015

## Slide 2
Declaring of compliance:
regulations containing mandatory analytical parameters
Technical Regulation for Safety of Foodstuffs of the Customs Union (TP TC 021/2011), Annex # 3, item # 8
Technical Regulation for Safety of Food Additives, Flavoring Substances & Processing Aids of the Customs Union (TP TC 029/2012), Annex # 8

## Slide 3
Declaring of compliance:
regulation containing mandatory requirements
Technical Regulation for Labelling of Foodstuffs of the Customs Union (TP TC 022/2011)

## Slide 4
# | Parameter | Maximum limit | Approved test method (standard) | Principle of the test method
1 | Lead (Pb), mg/kg | 0.3 | GOST 30178-96 | AAS
2 | Arsenic (As), mg/kg | 0.2 | GOST R 51766-01 | AAS
3 | Cadmium (Cd), mg/kg | 0.03 | GOST 30178-96 | AAS
4 | Mercury (Hg), mg/kg | 0.005 | GOST 26927-86 | Colorimetric determination (as copper tetraiodomercurate)/ AAS
5 | Total sulfur dioxide (SO2), mg/dm3 | 300.0 (according to product type) | GOST 32115-2013 | Oxidation of sulfurous acid by iodine
General mandatory analytical parameters: Safety
all kind of wine & wine products
declaration of compliance
participants: Federal Customs Service (FTS), importers, certification bodies, ISO accredited test labs
frequency of testing: each time for shipment or once per contract (e.g. in case of serial production)
Notes:
GOST = Interstate standard of the Commonwealth of Independent States (CIS)
GOST R = National standard of the Russian Federation

## Slide 5
# | Parameter | Limits | Approved test method (standard) | Principle of the test method
1 | Ethanol, % vol. | 8.5-22.0 | GOST 32095-2013 | Areometry after distillation
2 | Sugars, g/dm3 | According to product type | GOST 13192-73 | Bertrand's method/ Direct titration with Feling’s reagent
3 | Organoleptic properties | According to product type | GOST 32051-2013 | Organoleptic testing
4 | CO2 pressure | Sparkling wines | GOST 12258-79 | Aphrometer
Note:
GOST = Interstate standard of the Commonwealth of Independent States (CIS)
General mandatory analytical parameters: Identification
all kind of wine & wine products
declaration of compliance
participants: Federal Customs Service, importers, certification bodies, ISO accredited test labs
frequency of testing: each time for shipment or once per contract (e.g. in case of serial production)

## Slide 6
State market control and supervision of quality, safety & labelling of foodstuffs:
regulations containing mandatory requirements
Technical Regulation for Safety of Foodstuffs of the Customs Union (TP TC 021/2011)
Technical Regulation for Safety of Food Additives, Flavoring Substances & Processing Aids of the Customs Union (TP TC 029/2012)
Technical Regulation for Labelling of Foodstuffs of the Customs Union (TP TC 022/2011)
General sanitary, epidemiologic and hygienic requirements for the goods which are subject to sanitary and epidemiological supervision (control) of the Customs Union (May 28, 2010, # 299; last changes in May 15, 2013)

## Slide 7
# | Parameter | Maximum limit | Approved test method (standard) | Principle of the test method
1 | Pesticides | According to general regulations | GOST R 53971-2010 | Capillary electrophoresis
2 | Phthalates | 0.1 μg/l, 6 μg/l | MUK 4.1.738-99 | GC-MS
Note:
GOST R = National standard of the Russian Federation
MUK = Methodical instructions of the Rospotrebnadzor
Examples of special analytical parameters: Safety
all kind of wine & wine products
state control & supervision of goods on the market & production
participants: Federal Service for Customers’ Rights Protection and Human Well-Being Supervision (Rospotrebnadzor) & ISO accredited labs of the Rospotrebnadzor, producers, trade organizations, consumers
frequency of testing: scheduled inspections - once per 3 years & company according to the published plans/not scheduled inspections – day notification/according to complaints

## Slide 8
# | Parameter | Limits | Approved test method (standard) | Principle of the test method
1 | Citric acid | According to the relevant GOST or GOST R standards for specific groups of wines & wine products | GOST 32113-2013 | Enzymatic
2 | Titrable acids (as tartaric acid) |  | GOST 32114-2013 | Titration (pH 7.0)
3 | Volatile acids (as acetic acid) |  | GOST 32001-2012 | Titration after distillation
4 | Normalized extract |  | GOST 32000-2012 | Pycnometry
5 | Iron |  | GOST 13195-73/ GOST R 51823-2001 | Colorimetry/Inverse voltamperometry
6 | CO2 pressure |  | GOST 12258-79 | Aphrometer
7 | Sorbic acid |  | GOST 26181-84 | Spectrophotometry
8 | Ratio of carbon isotopes 13C/12C (wine ethanol & sugars) | GOST 32710-2014 | GOST 32710-2014 | IRMS/SIRA
Note:
GOST R = National standard of the Russian Federation
GOST = Interstate standard of the Commonwealth of Independent States (CIS)
Examples of special analytical parameters: Identification
all kind of wine & wine products
state control & supervision of goods on the market & production
participants: Federal Service for Alcohol Market Regulation (Rosalcoholregulirovanye) & ISO accredited lab of the Rosalcoholregulirovanye, Federal Service for Customers’ Rights Protection and Human Well-Being Supervision (Rospotrebnadzor) & ISO accredited labs of the Rospotrebnadzor, producers, trade organizations, consumers
frequency of testing: scheduled inspections - once per 3 years & company according to the published plans/not scheduled inspections – day notification/according to complaints

## Slide 9
Acceptance of test reports of ISO accredited labs:
actual state - acceptance of test reports of ISO accredited labs from the Customs Union (EAEC) only
since 2016 – participation of the Federal Service for Accreditation (Rosakkreditazya) in the ILAC agreement
bilateral memorandums of cooperation with 11 countries, including 1 APEC economy – Vietnam (main topics of the cooperation - informational and analytical exchange, training and skills development)

## Slide 10
Measures for market protection (import wine shipments rejections):
the market situation regarding the rejection of wine deliveries because of inappropriate quality or safety is rather stable
the rejection rate of import wine within two testing levels: - declaring of compliance – 1-5 % (depending on region), - state control & supervision – 1-2 cases (wine recalls) per year.

## Slide 11
Content of the publication:
legislation
limits
phthalates types
test methods
migration tests
phthalate in different materials contacting with wines & spirits
prevention of risks of contamination
toxicological roles of phthalates
Phthalates: published recommendations for prevention of contamination
Authors: Chatonnet P., Boutou S., Plana A.
Title: “Contamination of wines and spirits by phthalates: types of contaminations present, contamination sources and means of prevention”
Journal: Food Additives & Contaminants: Part A, 2014.- vol. 31.- No. 9.- p. 1605-1615
D.O.I. of the publication - http://dx.doi.org/10.1080/19440049.2014.941947

## Slide 12
Detailed information about system of the confirmation of wine compliance and technical regulation in the Russian Federation – see report “Russian Federation: Testing of wine for regulatory compliance and product safety” (APEC WRF Technical Workshop, November 4-6, 2013 in Washington, D.C.)

## Slide 13
THANK YOU FOR ATTENTION