## Slide 1
APEC Wine Regulatory Forum
Adelaide | Australia
Sulphur Dioxide in Wine
Ling Tian–GuangDong CIQ , AQSIQ, P. R. China
APEC WRF November 2015 | Adelaide Australia

## Slide 2: Determination of Total Sulfur dioxide(SO2) in Grape Wine
SO2 Function:
Multiple and diverse properties:
Antispetic agent, antioxidant and as a solvent, more can be clarification agent.
SO2 mainly used on three occasions:
(1) prefermentation step to prevent grape’s oxidation;
(2) before the ageing or storage steps, to inhibit microbial;
(3) before bottling, to stabilise wine and prevent any alteration or accident in the bottles.

## Slide 3: Determination of Total Sulfur dioxide(SO2) in Grape Wine
Negative effect:
Health:
For intolerance or high sensitivity to sulphites’ consumers, almost 1% of the population and 5% of the asthmatics are concerned.
The symptoms: flush face, rash, red and itchy skin, headaches, eye,face,lip or throat swelling; difficulty for breathing and so on.
Organoleptic alterations:
Undesirable aromas from sulphurous gas or from the reduction production, hydrosulphate and mercaptanes

## Slide 4: Determination of Total Sulfur dioxide(SO2) in Grape Wine
Limited Standards
OIV ranges from 150 to 400 mg/L of total SO2 (OIV-MA-C1-01), depend on the wine type, 2011 Issue.
P. R.China ranges from 0 to 250 mg/L , special for sweet grape wine and other fruit wine need to be under 400 mg/L (GB2760-2014), 2014 issue.

## Slide 5: Determination of Total Sulfur dioxide(SO2) in Grape Wine
Analytical methods of wine and fruit wine (GB/T 15038-2006)
Definitions
Total sulfur dioxide is difined as the total of all the various forms of sulfur dioxide present in the wine, either in the free state or combined with their constituents.
Principle
In alkaline condition, the combined sulfur dioxide will be released, become free sulfur dioxide. Then the total free sulfur dioxide is determined by direct titration with iodine.

## Slide 6
Regents
Sodium hydroxide solution (100g/L);
Iodine solution (0.02mol/L);
Sulfuric acid solution (1+3): add 1 volume concentrated sulfuric acid to 3 volume water, then get the dilute sulfuric acid solution.
Starch solution (10g/L);
Determination of Total Sulfur dioxide(SO2) in Grape Wine

## Slide 7
Procedure
Add 25ml sodium hydroxide solution into iodine flask (250ml), then add sample wine (25.00ml , 20℃) into iodine flask, need put the end of the pipet into the sodium hydroxide solution, shake and allow stand for 15mins, then add into a little bit ice, adding 1ml starch solution, 10 ml Sulfuric acid solution, stirring vigorously and immediately titrate with iodine solution (0.02mol/L),
Determination of Total Sulfur dioxide(SO2) in Grape Wine

## Slide 8
until the blue color persists clearly for 30 seconds. Let V mL the volume of iodine solution used.
Use water instead of sample wine, then do the blank experiment, Let V0 mL volume of iodine solution used.
Determination of Total Sulfur dioxide(SO2) in Grape Wine

## Slide 9
Expression of the results
X means content of total sulfur dioxide (mg/L);
c means content of iodine solution (mol/L);
V means the volume of iodine used (ml) of titrated the sample wine;
V0 means the volume of iodine used (ml) of titrated water;
32 means the molar mass of sulfur dioxide;
25 means the volume of the sample wine.
Determination of Total Sulfur dioxide(SO2) in Grape Wine

## Slide 10: Determination of Total Sulfur dioxide(SO2) in Grape Wine
Precisions:
Under the repeated condition, the difference’s absolute value of the results of two independ testing
should be under 10% of the average of the results of the two indpend testing.
∣X1-X2∣≤ , X1 and X2 means the results of two indepent testing, respectively.

## Slide 11: Thanks for your attention! tianling2008@yahoo.com 409232198@qq.com