## Slide 1: Heavy Metal in Wine
State Key Testing Laboratory of Wine and Alcohol Beverage
Ling TIAN , Ph.D.
September 11, 2014

## Slide 2: Content
View of the Key Lab;
Heavy Metal in Wine;
In future/advices.

## Slide 3: View of the Lab
Our Histroy
The wine testing laboratory was established and operated in 2010 in Huangpu, Guangdong Entry-Exit Inspection and Quarantine Bureau (CIQ).
The lab was approved to be state key wine testing laboratory in 2011, by General Administration of Quality Supervision, Inspection and Quarantine of the People’s Republic of China (AQSIQ).

## Slide 4: Our Building

## Slide 5
Accreditation
State Key testing Laboratory of wine and Alcohol Beverage (Guangdong) is accredited by CNAS-CL01 (China National Accreditation Service for Conformity Assessment, CNAS), which is equal to (ISO/IEC17025:2005).
Our current Scope of Accreditation for the lab’s facility covers all methods which is concerning China’s standard of grape wine.

## Slide 6: Technical Platform of the Lab
Instrumental platform
Wet Chemistry
IRMS
(Flash EA, Gas Bench, GC-Isolink, LC-ISOlink)
GC/GC-MS
Inorganic tools (ICP/ICP-MS/AES)
Microbiology
LC/ LC-MS

## Slide 7
Wet chemistry: alcohol, dry extract, sugar, acid, etc.
GC/GC-MS: Plasticizer, Pesticides, aroma compounds, etc.
LC/LC-MS: Mycotoxin, biogenic amines, amino acids, food addictives, polyphenols, etc.
Technical Platform of the Lab

## Slide 8
IRMS(Flash EA, Gas Bench, etc.): Authenticity/determination the isotope ratio of 18O/16O, 13C/12C, 2H/1H, etc.
Inorganic tools (ICP/ICP-MS) : Mineral elements(Cu、 Fe、 Pb、 Zn, etc.);
Microbiological methods: Bacteria and Pathogens (Total bacterial count, Coliforms, Salmonella, Shigella, Staphylococcus aureus, etc. );
Technical Platform of the Lab

## Slide 9: Heavy Metal in Wine/ Background
Along with P.R.China’s recent and fast economic development, the Chinese wine sector experiences substantial changes.
From 2003 to 2013, wine production increased from 343.2 to 1382.1ML(Million liter) (302%), also sharp increasing of wine imports (including bottled wine, bulk wine and sparkling wine) from 41.2 ML to 376.8ML.

## Slide 10
Heavy Metal in Wine/ Background
Chart: 
| Chinese wine production | Import wine (Million Liter)
2003 | 343.2 | 41.2
2013 | 1382.1 | 376.8

## Slide 11
Meanwhile, the consumption volume of alcoholic beverages greatly increased in China: China has replaced France and became the No.1 of wine consumption economy in 2013.
Heavy Metal in Wine/ Background

## Slide 12
Concerning too much the Food safety issues happened, also the wine’s safety also aroused too much interest.
Metal content also is one of the risk factors, although the trace elements are essential for humans, many of them (e.g., Cu, Bi, Sn, As, Pb) have unknown biological function and are toxic, because they accumulated in the human organism.
In fact, at slightly higher levels than when found in living beings, they can have toxic effects.
Heavy Metal in Wine/ Background

## Slide 13: Heavy Metal Poisoning

## Slide 14
Source:
1). The primary natural metal content of wines is determined by many factors, such as the type of soil, the variety of grape, the weather conditions, the pollution, and viticultural practices.
2). The secondary mineral contamination is derived from the use of pesticides and fertilizers or acquired during winemaking.
Heavy Metal in Wine/ Background

## Slide 15: Limit Standards
No. | Metal (Chinese Standard) | Chinese standards | Metal (OIV Standard) | OIV Standard
1 | Copper (Cu) | ≤1.0mg/L | Arsenic (As) | ≤0.2mg/L
2 | Iron (Fe) | ≤8.0mg/L | Cadmium (Cd) | ≤0.01mg/L
3 | Lead (Pb) | ≤0.2mg/L | Copper (Cu ) | ≤1.0mg/L
4 | Manganese (Mn) | ≤2.0mg/L | Lead (Pb) | ≤0.15 mg/L
5 |  |  | Zinc (Zn) | ≤5mg/L

## Slide 16: Testing Methods
No. | Metal (Chinese Standard) | Chinese standards | Metal (OIV Standard) | OIV Standard
1 | Copper (Cu) | GB15038-2006 | Arsenic (As) | OIV-MA-AS323-01A/B(AAS)/C(Colorimetry)
2 | Iron (Fe) | GB15038-2006 | Cadmium (Cd) | OIV-MA-AS322-10
3 | Lead (Pb) | GB5009.12-2010 | Copper (Cu ) | OIV-MA-AS322-06
4 | Manganese (Mn) | GB/T 5009.90-2003 | Lead (Pb) | OIV-MA-AS322-12
5 |  |  | Zinc (Zn) | OIV-MA-AS322-08

## Slide 17: Case1-Heavy Metal In Wine
Sample: 94 bottles of wine from different economies/area;
Methods: Chinese testing Standard and ICP-AES;
Metal: Copper (Cu), Iron (Fe), Lead (Pb),Manganese (Mn), Arsenic (As), Cadmium(Cd), Zinc (Zn).

## Slide 18: Case1-Metal In Wine
Metal | Copper (Cu) | Iron (Fe) | Lead (Pb) | Manganese (Mn) | Arsenic (As) | Cadmium (Cd) | Zinc (Zn)
Over Standard | 0% | 2.13% | 0% | 13.83% | 0% | 0% | 0%
Result:

## Slide 19: In Future/advices
Based on the metal’s toxic effects and its resource, we need to track the metal of wine, also make sure the results’s reliability. There are two advices:
1). Ring tests;
2). Research project: Heavy Metal In Wine;

## Slide 20: Heavy Metal In Wine

## Slide 21: Heavy Metal In Wine

## Slide 22: Thanks for your attention!