## Slide 1: Sugar Testing Method for Wine
Ni Xinlu
Shanghai entry-exit inspection and quarantine bureau
September 11, 2014

## Slide 2: Contents
1、The standards related to sugar in wine
2、The testing methods of residual sugar in wine
3、 Questions/Advices

## Slide 3: National standards related to the wine
GB 2758-2012 “Fermented alcoholic beverages and their integrated alcoholic beverages”
GB 7718-2011"General standard for the labeling of prepackaged foods”
GB15037-2006 “Wine”

## Slide 4: National standards related to the wine
GB15037-2006 “Wine”
  It took effect on Jan.1,2008 as a mandatory standard.
  The standard covers requirements for all processes from grape planting, wine production to its transportation.
  Definitions : Various types of wine corresponding requirements for the sugar content, vintage wines, varietal wines, and original wines.
  Regulate the use of additives in wine .
  Part of this standard definitions equivalent adopted OIV regulations(2003 edition).

## Slide 5: Wine type judgement principle from sugar content (GB 15037-2006“wine”)
ITEM |  |  | Requirement
Total sugar d（As Glucose）/(g/L) | Still wine | Dry wine b | ≤4.0
 |  | Semi-dry wine c | 4.1~12.0
 |  | Semi-sweet wine | 12.1~45.0
 |  | Sweet wine | ≥45.1
 | Sparkling wine | Brut sparkling wine | ≤12.0（Tolerance of 3.0）
 |  | Extra-dry sparkling wine | 12.1~17.0（Tolerance of 3.0）
 |  | Dry sparkling wine | 17.1~32.0（Tolerance of 3.0）
 |  | Semi-dry sparkling wine | 32.1~50.0
 |  | Sweet sparkling wine | ≥50.1
b. When difference between the total sugar and total acid (As tartaric acid) is less than or equal to 2.0 g/L, the total sugar should be up to 9.0 g/L. c. When difference between the total sugar and total acid (As tartaric acid) is less than or equal to 2.0 g/L, the total sugar should be up to 18.0 g/L。 d. The requirement of the total sugar in semi-sparkling wine is the same as in still wine. |  |  | 

## Slide 6: Contents
1、The standards related to sugar in wine
2、The testing methods of residual sugar in wine
3、 Questions/Advices

## Slide 7: The testing method of total sugar and total acid in wine
GB/T 15038-2006
“General analytical methods of grape wine and fruit wine”

## Slide 8: The testing method of total sugar in wine
Principle：

## Slide 9: The testing method of total sugar in wine：Titration
Mix the Fehling solution A and B (standardized beforehand)
Add a amount of samples hydrolysis solution
Titrate with Glucose standard solution
boiling
End-point: potential mutation
or methylene blue colour fading
Procedure

## Slide 10: The testing method of total acid in wine
Principal：
Wine is titrated by Sodium hydroxide standard solution to end-point (pH = 8.2) or till phenolphthalein indicator changes to pink, total acid content can been calculated with the consumption of sodium hydroxide.

## Slide 11: Definitions of Residual SUGAR in wine
Residual sugar
Total sugar
Glucose+Fructose+other oligosaccharides (can been hydrolysised to the reducing sugar)+other reducing matter(e.g.tannin polyphenols)
GB 15037、GB/T15038
Reducing sugar
Glucose+Fructose
OIV etc.
Notes: Complementary definitions relating to carbon dioxide content (18/73), (Oeno 1/02)
The wine is said to be :
Still, when the carbon dioxide concentration is less than 4 g/l at 20°C,
Semi-sparkling, when this concentration is equal to or above 3 g/l and less than or equal to 5 g/l at 20°C.
Sparkling wines 起泡葡萄酒
The wine is said to be :
brut when it contains at the most 12 g/l of sugar with a tolerance of + 3 g/l;
extra-dry, when it contains at least 12 g/l and at most 17 g/l with a tolerance of + 3 g/l;
dry, when it contains at least 17 g/l and at most 32 g/l with a tolerance of +3 g/l;
demi-sec, when it contains 32 to 50 g/l;
sweet, when it contains more than 50 g/l.

## Slide 12: Different testing methods
Method | China | e.g. OIV
Method of residual sugar | Titration based on REDOX reaction | Enzymatic method or HPLC
Method of total acid | Titration (End-point is pH 8.2 or Phenolphthalein indicator show pink) | Titration (End-point is pH 7.0 or Bromothymol indicator show blue-green)

## Slide 13: Comparing the sugar results of different methods
Sample No. | Wine type | Titration （as glucose） Automatic potentiometric titration | Flow Injection Analysis （as glucose） | Enzymatic method （glucose+fructose） | HPLC method (glucose+fructose)
1 | Dry | 2.5 | 1.9 | 0.23 | 0.50
2 | Dry | 3.4 | 2.4 | 0.26 | 0.48
3 | Dry | 3.0 | 2.3 | 0.15 | 0.33
4 | Dry | 2.9 | 2.7 | 0.30 | 0.50
5 | Dry | 1.7 | 2.1 | 1.4 | 1.25
6 | Dry | 1.5 | 1.6 | 0.28 | 0.57
7 | Dry | 6.4 | 6.3 | 3.5 | 3.7
8 | Dry | 7.0 | 8.5 | 6.1 | 5.7
9 | Dry | 6.3 | 16.5 | 12.0 | 11.4
10 | Dry | 6.4 | 10.0 | 7.6 | 6.5
g/L

## Slide 14: The sugar results of dry-wine
Chart: 
| sample1-dry | sample2-dry | sample3-dry | sample4-dry | sample5-dry | sample6-dry | sample7-dry | sample8-dry | sample9-dry | sample10-dry
Titrator | 2.5 | 3.4 | 3 | 2.9 | 1.7 | 1.5 | 6.4 | 7 | 6.3 | 6.4
Flow | 1.9 | 2.4 | 2.3 | 2.7 | 2.1 | 1.6 | 6.3 | 8.5 | 16.5 | 10
Enzymatic | 0.23 | 0.26 | 0.15 | 0.3 | 1.37 | 0.28 | 3.5 | 6.1 | 12 | 7.6
HPLC | 0.496 | 0.478 | 0.331 | 0.496 | 1.246 | 0.572 | 3.7 | 5.7 | 11.4 | 6.5
g/L

## Slide 15: Conclusion
For dry wine，the sugar results of Enzymatic method and HPLC method are similar. The sugar results of Titration method and Flow method are similar.
For dry wine, the sugar results of Titration method and Flow method are higher than Enzymatic method and HPLC method.

## Slide 16: Comparing the sugar results of different methods
Sample No. | Wine type | Titration （as glucose） Automatic potentiometric titration | Flow Injection Analysis （as glucose） | Enzymatic method （glucose+fructose） | HPLC method (glucose+fructose)
11 | Semi-dry | 7.2 | 16.0 | 2.4 | 12.2
12 | Semi-dry | 8.2 | 9.3 | 8.1 | 7.95
13 | Semi-sweet | 12.8 | 16.0 | 11.7 | 15.0
14 | Semi-sweet | 33.5 | 42.0 | 37.1 | 35.2
15 | sweet | 51.3 | 51.0 | 47.5 | 48.8
16 | sweet | 96.9 | 131 | 130 | 115
g/L

## Slide 17: The sugar results of semi-dry wine and semi-sweet wine
Chart: 
| sample7-semi dry | sample8-semi dry | sample9-semi sweet | sample10-semi sweet
Titrator | 7.2 | 8.2 | 12.8 | 33.5
Flow | 15.7 | 9.3 | 16.2 | 42
Enzymatic | 2.42 | 8.09 | 11.68 | 37.09
HPLC | 12.175 | 7.952 | 14.993 | 35.187
11
12
13
14
g/L

## Slide 18: The sugar results of sweet wine
Chart: 
| sample11-sweet | sample12-sweet
Titrator | 51.3 | 96.9
Flow | 50.8 | 131
Enzymatic | 47.49 | 129.5
HPLC | 48.756 | 115.142
15
16
17
g/L

## Slide 19: Conclusion
For the wine with high sugar content , the sugar results of four different methods change irregularly.

## Slide 20: The total acid results of dry-wine
Sample No. | Wine type | End-point pH8.2 | End-point pH7.0
7 | dry | 5.01 | 4.62
8 | dry | 7.57 | 7.16
9 | dry | 6.18 | 5.56
10 | dry | 6.22 | 5.85
Chart: 
| sample7-dry | sample8-dry | sample9-dry | sample10-dry
pH8.2 | 5.01 | 7.57 | 6.18 | 6.22
pH7.0 | 4.62 | 7.16 | 5.56 | 5.85
Conclusion The total acid results of the method(end-point pH=8.2)are higher than the method(end-point pH=7.0) obviously.
g/L

## Slide 21: One of the inconformity of imported wine
Product do not reflect its true nature(such as total sugar do not match the label).
The non-conformance with the wine label caused by the sugar content occurs intermittently.

## Slide 22: Contents
1、The standards related to sugar in wine
2、The testing methods of residual sugar in wine
3、 Questions/Advices

## Slide 23: Questions/Advices
Lable: Wine type
1.How to reach consensus about judgement principle based on residual sugar content？
2.Definition of residual sugar in wine.
Ring test:
On the above basis, ring test can make sure the results’s reliability.

## Slide 24
Thanks for your attention